G=H*( kp+Ki over s+kds ) over {1+kbH( kp+ki over s+kds)} general PID of any order
when H=kh over{ 1+%tau s } for 1st order process

G ={kd s^2 +kp s+ki} over {s over H +kb(kd s^2 +kp s+ki )} newline G = {kd s^2 +kp s+ki} over {s( 1+%tau S ) over kh+kb(kd s^2 +kp s+ki )} newline G={kd s^2 +kp s+ki} over {(kb kd +%tau over kh )s^2 +(kb kp+ 1 over kh )s+kbki }
for kd=0, kb=1
G={kp s+ki} over {%tau over kh s^2 +(kp+ 1 over kh)s+ki }
with step c/s
L=G c over s=c over s {kp s+ki} over {%tau over kh s^2 +(kp+ 1 over kh)s+ki } newline L=c over s {s+ki over kp} over {%tau over {kh kp} s^2+{kpkh+ 1 }over {kpkh} s+ki over kp } newline L=c kpkh over %tau {s+ki over kp} over {s (s^2+(kpkh+ 1) over %tau s+kikh over %tau ) }
from 28a
{s+ %alpha }over {s(s^2+2 %zeta %omega s +%omega ^2) }=%alpha over %omega ^2 +1 over { %omega sqrt{1-%zeta ^2} }sqrt{(%alpha over %omega-%zeta )^2+(1-%zeta^2)} e^(-%zeta %omega t) sin( %omega sqrt{1-%zeta^2} t +%phi )
%phi=atan2( %omega sqrt{1-%zeta^2},%alpha -%omega %zeta )-atan2( sqrt{1-%zeta^2},-%zeta )
%omega=sqrt {kikh over %tau} newline 2 %zeta %omega=( kpkh+1 ) over %tau newline %zeta=( {kpkh+1} over {2 %tau} )sqrt{ %tau over kikh }={ kpkh+1} over{2 sqrt{kikh %tau}}
if ζ>1 then use exponential form 11
{s+%alpha }over {s(s+a)(s+b) }=1 over { ab } left [ %alpha-{b(%alpha -a)}over{b-1}e^{-%alpha t}+ {a(%alpha -b)over{b-a}}e^{-bt} right ]
let ab=m,a+b=n;
 ab=kikh/τ, a+b=(kpkh+1)/ τ,
a+m/b=n;
a^2-na+m=0; a=(n+-sqrt(n^2-4m))/2;

there is 2 solution when overdamp ,need to figure out which one is correct
1st order PID
G={kd s^2 +kp s+ki} over {(kb kd +%tau over kh)s^2 +(kb kp+ 1 over kh)s+kbki } newline G*c over s={c kd} over {kbkd+%tau over kh} {s^2 +kp over kd s+ki over kd} over {s(s^2 +(kb kp+ 1 over kh)over{kbkd+%tau over kh}s+kbki over{kbkd+%tau over kh}) } equation 36 and 35

equation 35
{s^2+%alpha rsub{1} s+%alpha rsub{0} } over {s(s+a)(s+b) }={s^2+%alpha rsub{1} s+%alpha rsub{0} } over {s(s^2+(a+b)s+ab) } newline %alpha rsub{1} =kp over kd newline %alpha rsub{ 0 }=ki over kd newline ab=kikb over { kbkd+%tau over kh } newline a+b={ kbkp+1 over kh} over{ kbkd+%tau over kh} newline let m=ab , n=a+b newline b=m over a newline a+m over a=n newline a^2-na+m=0 newline a={n +-sqrt{ n^2-4m } } over 2
only the + root is correct ,conform by plotting the two line

equation 36
{s^2+%alpha rsub{1} s+%alpha rsub{0} } over {s(s+a)^2+b^2}={s^2+%alpha rsub{1} s+%alpha rsub{0} } over {s(s^2+2as+a^2+b^2) } newline a^2+b^2=ki over { kbkd+%tau } newline 2a={ kbkp+1 } over{ kbkd+%tau }
a={kbkp+1} over{2(kbkd+%tau) } newline b= +- sqrt{a^2+ki over{kbkd+%tau}}

or convert to the zeta omega form as below
{s^2+%alpha rsub{1} s+%alpha rsub{0} } over {s(s+a)^2+b^2}={s^2+%alpha rsub{1} s+%alpha rsub{0} } over {s(s^2+2as+a^2+b^2) }={s^2+%alpha rsub{1} s+%alpha rsub{0} } over {s(s^2+2%zeta %omega s+%omega ^2) } newline a^2+b^2=c^2=kikb over { kbkd+%tau over kh }=%omega^2 newline 2a={ kbkp+1 over kh } over{ kbkd+%tau over kh }=2%zeta %omega newline a={ kbkp+1 over kh} over{2( kbkd+%tau over kh) }=%zeta %omega newline %zeta^2 w^2+b^2=w^2 newline b^2=w^2-%zeta^2 w^2 newline b=w sqrt{ 1-%zeta^2 } newline %omega=sqrt{ kikb over{kbkd +%tau over kh} } newline %zeta={kbkp+1 over kh} over {2w( kbkd+%tau over kh)}
Zeta 1+KhKbKp / [2sqrt(t+KhKbKd)(KhKbKi)]
inverse of laplace equation 36 is
{%alpha rsub{0} }over c^2+1 over{ bc } left [ (a^2-b^2-%alpha rsub{1} a+%alpha rsub{0} )^2+b^2(%alpha rsub{1}-2a)^2 right ]^{1/2 } e^{ -at } sin( bt+%phi ) newline {}={%alpha rsub{0} }over %omega ^2+1 over{%omega^2 sqrt{1-%zeta^2} } left [ (%zeta^2 %omega^2-%omega^2 (1-%zeta^2)-%alpha rsub{1} %zeta %omega+%alpha rsub{0} )^2+%omega^2 (1-%zeta^2)(%alpha rsub{1}-2 %zeta %omega)^2 right ]^{1/2 } e^{ -%zeta %omega t } sin({%omega sqrt{1-%zeta^2} }t+%phi ) newline
%phi=atan2 left ( b(%alpha rsub{1} -2a),a^2-b^2-%alpha rsub{1}a+%alpha rsub{0} right )- atan2 left ( b,-a right ) newline { }=atan2 left ( %omega sqrt{1-%zeta^2}(%alpha rsub{1} -2%zeta %omega),%zeta^2 %omega^2-%omega^2(1-%zeta^2)-%alpha rsub{1}%zeta %omega+%alpha rsub{0} right )- atan2 left ( %omega sqrt{1-%zeta^2},-%zeta %omega right )